12 July 2004, Vityaz’ Bay (Figures 1-3).

Ground truth measurements were carried out at Cape Shults and Popov Island as well as at several coastal and island points before, during and after ENVISAT and ERS-2 overpasses. Acquisition of wind speed and direction, air temperature and humidity and water temperature at Cape Shults was carried out from a pier, a coastal vantage point and from a yacht. Sea surface roughness characteristics were measured with a system of light floats and with single float and calibration spheres as well as with a developed polarization spectrophotometer at Cape Shults station.

Wind speed W = 3-5 m/s, racing L = 3 km. The regular one-dimensional sea surface roughness was observed (Figure 3a). It was characterized by a main maximum at frequency near 0.7 Hz and the basic wavelength 3.2 m.

Figure 1. Image of the sea surface taken by Pixelfly camera, F = 50 mm with V-polarization on 12 July 2004 at 01:40 UTC during Envisat ASAR sensing (a) and spatial autocorrelation function computed for rectangle area the size of 24 x 24 m (b). Diameter of the float 23 cm, distance between camera and float D = 436 m.

Figure 2. Retrieved wave height (a), correlation function (b), power spectral density (c) and normalized power spectral density (d) computed for realization consisting of 2000 points. Slope of green line  = -4 and slope of red line  = -5. Measurements were conducted on 12 July 2004 at 1:30 UTC during Envisat ASAR sensing.

Figure 3. Characteristics of the sea surface derived from the measurements of the brightness of the sea surface taken by Pixelfly camera, F = 50 mm with V-polarization on 12 July 2004 at 01:35 UTC during Envisat ASAR sensing. Spectra were computed by processing of 2000 points. Slope of green line  = -4 and slope of red line  = -5.